| Pos. | Quantity | Designation | Item price EUR | Total price EUR |
| --- | --- | --- | --- | --- |
|  |  | EIGERFLEX® cold water pipe DN 20 – 40 (ø 25 – 50 mm) suitable up to max. 30°C and 16 bar, longitudinally watertight, comprising: medium pipe in PE100, a continuously foamed-in self-regulating frost protection strip, aluminum adhesive tape for heat distribution, insulation made of continuously manufactured CFC-free, CO2-blown flexible rigid polyurethane foam, PE foil and a sinusoidally corrugated, seamlessly extruded-on polyethylene (LLD-PE) outer casing, including factory test. Delivered on drums or in rings. EIGERFLEX® cold water pipe cont. m EIGERFLEX® 25/76 3/4" DN 20 cont. m EIGERFLEX® 32/76 1" DN 25 cont. m EIGERFLEX® 40/91 1 1/4" DN 32 cont. m EIGERFLEX® 50/91 1 1/2" DN 40 |  |  |

| Pos. | Quantity | Designation | Item price EUR | Total price EUR |
| --- | --- | --- | --- | --- |
|  |  | EIGERFLEX® cold water pipe DN 50 – 100 (ø 63 – 110 mm) suitable up to max. 30°C and 16 bar, longitudinally watertight, comprising: medium pipe in PE100, a continuously foamed-in self-regulating frost protection strip in the frost protection strip channel, aluminum adhesive tape for heat distribution, insulation made of continuously manufactured CFC-free, CO2-blown flexible rigid polyurethane foam, PE foil and a sinusoidally corrugated, seamlessly extruded-on polyethylene (LLD-PE) outer casing, including factory test. Delivered on drums or in rings. EIGERFLEX® cold water pipe cont. m EIGERFLEX® 63/126 2" DN 50 cont. m EIGERFLEX® 75/126 2 1/2" DN 65 cont. m EIGERFLEX® 90/162 3" DN 80 cont. m EIGERFLEX® 110/162 4" DN 100 * further dimensions on request |  |  |

| Pos. | Quantity | Designation | Item price EUR | Total price EUR |
| --- | --- | --- | --- | --- |
|  |  | EIGERFLEX® house lead-in bend, 90° Leg length 1.1 x 1.6m. longitudinally watertight, medium pipe in PE-HD, foamed-in self-regulating frost protection strip, aluminum adhesive tape for heat distribution, insulation made of CFC-free CO2-blown rigid polyurethane foam, protective casing in polyethylene (PE-HD). EIGERFLEX bend® Unit: EIGERFLEX® 25/76 3/4" DN 20 Unit: EIGERFLEX® 32/76 1" DN 25 Unit: EIGERFLEX® 40/91 1 1/4" DN 32 Unit: EIGERFLEX® 50/91 1 1/2" DN 40 Unit: EIGERFLEX® 63/126 2" DN 50 Unit: EIGERFLEX® 75/126 2 1/2" DN 65 Unit: EIGERFLEX® 90/162 3" DN 80 Unit: EIGERFLEX® 110/162 4" DN 100 |  |  |

| Pos. | Quantity | Designation | Item price EUR | Total price EUR |
| --- | --- | --- | --- | --- |
|  |  | EIGERFLEX® sealing ring consisting of a specially profiled neoprene ring, suitable for: Outer diameter of EIGERFLEX® 76 mm Outer diameter of EIGERFLEX® 91 mm Outer diameter of EIGERFLEX® 111 mm Outer diameter of EIGERFLEX® 126 mm Outer diameter of EIGERFLEX® 142 mm Outer diameter of EIGERFLEX® 162 mm Sealing ring for wall leadthrough, impermeable to water pressure < 0.5 bar, seal insert type A (centering) and type C40 (sealing) for core bore or pipe liner, suitable for: Outer diameter of EIGERFLEX® 76 mm Outer diameter of EIGERFLEX® 91 mm Outer diameter of EIGERFLEX® 111 mm Outer diameter of EIGERFLEX® 126 mm Outer diameter of EIGERFLEX® 142 mm Outer diameter of EIGERFLEX® 162 mm |  |  |

| Pos. | Quantity | Designation | Item price EUR | Total price EUR |
| --- | --- | --- | --- | --- |
|  |  | EIGERFLEX® shrink-on end cap for damp zones Heat-shrink closure for house lead-ins, consisting of: molecular cross-linked and modified polyolefin, coated with sealing adhesive with temperature resistance up to 125°C. Including temperature measuring strip and abrasive strip. or End cap for EIGERFLEX® for dry zones suitable for: Unit: EIGERFLEX® 25/76 3/4" DN 20 Unit: EIGERFLEX® 32/76 1" DN 25 Unit: EIGERFLEX® 40/91 1 1/4" DN 32 Unit: EIGERFLEX® 50/91 1 1/2" DN 40 Unit: EIGERFLEX® 63/126 2" DN 50 Unit: EIGERFLEX® 75/126 2 1/2" DN 65 Unit: EIGERFLEX® 90/162 3" DN 80 Unit: EIGERFLEX® 110/162 4" DN 100 |  |  |

| Pos. | Quantity | Designation | Item price EUR | Total price EUR |
| --- | --- | --- | --- | --- |
|  |  | EIGERFLEX® connecting piece, screwed connection to connect with onward pipes PE connecting piece in brass with external thread, suitable for: PE pipe DN external thread 25 x 2.3 mm 20 3/4" 32 x 2.9 mm 25 1" 40 x 3.7 mm 32 1 1/4" 50 x 4.6 mm 40 1 1/2" 63 x 5.8 mm 50 2" 75 x 6.8 mm 65 2 1/2" 90 x 8.2 mm 80 3" 110 x 10 mm 100 4" EIGERFLEX® coupling, screwed connection, equal in brass, to connect two EIGERFLEX® pipes (without insulation material), suitable for: PE pipe DN PE pipe DN 25 x 2.3 mm 20 25 x 2.3 mm 20 32 x 2.9 mm 25 32 x 2.9 mm 25 40 x 3.7 mm 32 40 x 3.7 mm 32 50 x 4.6 mm 40 50 x 4.6 mm 40 63 x 5.8 mm 50 63 x 5.8 mm 50 75 x 6.8 mm 65 75 x 6.8 mm 65 90 x 8.2 mm 80 90 x 8.2 mm 80 110 x 10 mm 100 110 x 10 mm 100 EIGERFLEX® coupling, screwed connection, reduced, in brass, to connect two EIGERFLEX® pipes (without insulation material), suitable for: PE pipe DN PE pipe DN 32 x 2.9 mm 25 25 x 2.3 mm 20 40 x 3.7 mm 32 32 x 2.9 mm 25 50 x 4.6 mm 40 40 x 3.7 mm 32 63 x 5.8 mm 50 50 x 4.6 mm 40 75 x 6.8 mm 65 63 x 5.8 mm 50 90 x 8.2 mm 80 75 x 6.8 mm 65 110 x 10 mm 100 90 x 8.2 mm 80 |  |  |
| Pos. | Quantity | Designation | Item price EUR | Total price EUR |
|  |  | EIGERFLEX®, T-piece, screwed connection for PE pipes (without insulating material) up to multiple-stage reduction, suitable for: Unit: 25-25-25 mm Unit: 32-32-32 mm Unit: 32-25-32 mm Unit: 32-25-25 mm Unit: 40-40-40 mm Unit: 40-32-40 mm Unit: 40-25-40 mm Unit: 40-32-32 mm Unit: 40-25-32 mm Unit: 50-50-50 mm Unit: 50-40-50 mm Unit: 50-32-50 mm Unit: 50-25-50 mm Unit: 50-40-40 mm Unit: 50-32-40 mm Unit: 50-25-40 mm Unit: 63-63-63 mm Unit: 63-50-63 mm Unit: 63-40-63 mm Unit: 63-32-63 mm Unit: 63-25-63 mm Unit: 63-50-50 mm Unit: 63-40-50 mm Unit: 63-32-50 mm Unit: 63-25-50 mm Unit: 75-75-75 mm Unit: 75-63-75 mm Unit: 75-50-75 mm Unit: 75-40-75 mm Unit: 75-32-75 mm Unit: 75-25-75 mm Unit: 75-63-63 mm Unit: 75-50-63 mm Unit: 75-40-63 mm Unit: 75-32-63 mm Unit: 75-25-63 mm |  |  |

| Pos. | Quantity | Designation | Item price CHF | Total price CHF |
| --- | --- | --- | --- | --- |
|  |  | EIGERFLEX®, T-piece, screwed connection continued Unit: 90-90-90 mm Unit: 90-75-90 mm Unit: 90-63-90 mm Unit: 90-50-90 mm Unit: 90-40-90 mm Unit: 90-32-90 mm Unit: 90-25-90 mm Unit: 90-75-75 mm Unit: 90-63-75 mm Unit: 90-50-75 mm Unit: 90-40-75 mm Unit: 90-32-75 mm Unit: 90-25-75 mm Unit: 110-110-110 mm Unit: 110-90-110 mm Unit: 110-75-110 mm Unit: 110-63-110 mm Unit: 110-50-110 mm Unit: 110-40-110 mm Unit: 110-32-110 mm Unit: 110-25-110 mm Unit: 110-90-90 mm Unit: 110-75-90 mm Unit: 110-63-90 mm Unit: 110-50-90 mm Unit: 110-40-90 mm Unit: 110-32-90 mm Unit: 110-25-90 mm |  |  |

| Pos. | Quantity | Designation | Item price EUR | Total price EUR |
| --- | --- | --- | --- | --- |
|  |  | EIGERFLEX®, Assembly T-piece Insulating material: PUR foam packing T-piece set with ABS half shells Comprising: two ABS half-shells incl. reduction rings (3 pc.) for the corresponding outer pipe diameters, venting plugs (3 pc.), glue (1 pc.), closing clamps (16 pc.), polyurethane foam bottled (1 pc.) suitable for: Unit: outer pipe, 76-76-76 mm Unit: outer pipe, 91-91-91 mm Unit: outer pipe, 91-76-91 mm Unit: outer pipe, 91-76-76 mm Unit: outer pipe, 111-111-111 mm Unit: outer pipe, 111-91-111 mm Unit: outer pipe, 111-76-111 mm Unit: outer pipe, 111-91-91 mm Unit: outer pipe, 111-76-91 mm Unit: outer pipe, 126-126-126 mm Unit: outer pipe, 126-111-126 mm Unit: outer pipe, 126-91-126 mm Unit: outer pipe, 126-76-126 mm Unit: outer pipe, 126-111-111 mm Unit: outer pipe, 126-91-111 mm Unit: outer pipe, 126-76-111 mm |  |  |
| Pos. | Quantity | Designation | Item price EUR | Total price EUR |
|  |  | EIGERFLEX®, Assembly T-piece Insulating material: PUR foam packing T-piece set with GFK half shells Comprising: two GFK half-shells in break-resistant glass fiber polyester (incl. reduction rings for the corresponding outer pipe diameters), screw valve in brass, sealing strip, screw set and packing Polyurethane foam, suitable for: Unit: outer pipe, 142-142-142 mm Unit: outer pipe, 142-126-142 mm Unit: outer pipe, 142-111-142 mm Unit: outer pipe, 142-91-142 mm Unit: outer pipe, 142-76-142 mm Unit: outer pipe, 142-126-126 mm Unit: outer pipe, 142-111-126 mm Unit: outer pipe, 142-91-126 mm Unit: outer pipe, 142-76-126 mm Unit: outer pipe, 162-162-162 mm Unit: outer pipe, 162-142-162 mm Unit: outer pipe, 162-126-162 mm Unit: outer pipe, 162-111-162 mm Unit: outer pipe, 162-91-162 mm Unit: outer pipe, 162-76-162 mm Unit: outer pipe, 162-142-142 mm Unit: outer pipe, 162-126-142 mm Unit: outer pipe, 126-111-142 mm Unit: outer pipe, 162-91-142 mm Unit: outer pipe, 162-76-142 mm |  |  |
| Pos. | Quantity | Designation | Item price EUR | Total price EUR |
|  |  | EIGERFLEX® joint set type EIGERFLEX®-EIGERFLEX® for 16 bar pipes, with insulating material: foam packing in polyurethane foam or PE foam, comprising: one PEH joint pipe (for reduction joints: reduced on one side), two PE shrink-on sleeves, foam packing in polyurethane foam or PE foam, and one abrasive strip. Joint set, EIGERFLEX®-EIGERFLEX® for EIGERFLEX® with PUR foam packing, to match the outer diameter: Unit: 76 mm to 76 mm Unit: 91 mm to 91 mm Unit: 91 mm to 76 mm Unit: 111 mm to 111 mm Unit: 111 mm to 91 mm Unit: 126 mm to 126 mm Unit: 126 mm to 111 mm Unit: 142 mm to 142 mm Unit: 142 mm to 126 mm Unit: 162 mm to 162 mm Unit: 162 mm to 142 mm |  |  |
| Pos. | Quantity | Designation | Item price EUR | Total price EUR |
|  |  | EIGERFLEX® joint set type EIGERFLEX®-EIGERFLEX® for EIGERFLEX® with PE foam, to match outer pipe diameters: Unit: 76 mm to 76 mm Unit: 91 mm to 91 mm Unit: 91 mm to 76 mm Unit: 111 mm to 111 mm Unit: 111 mm to 91 mm Unit: 126 mm to 126 mm Unit: 126 mm to 111 mm Unit: 142 mm to 142 mm Unit: 142 mm to 126 mm Unit: 162 mm to 162 mm Unit: 162 mm to 142 mm |  |  |
| Pos. | Quantity | Designation | Item price EUR | Total price EUR |
|  |  | EIGERFLEX® components for frost protection strip All components are intercoordinated; all liability is declined if non-specified components are used. EIGERFLEX® Thermostat UTR 15 Adjustment range –5°C to +15°C Switching current: 16 A Incl. temperature sensor (cable length: 3 m) EIGERFLEX® connection - heating strip/cold end, A-H/K Connection fitting between frost protection strip and cold end EIGERFLEX® end closure, heating strip EA-H End closure fitting for frost protection strip EIGERFLEX® connection - heating strip/heating strip, V-H/H Connection fitting between 2 frost protection strips EIGERFLEX® Micro Uni Clip Shrink-on set to connect 3 frost protection strips (T-piece). EIGERFLEX® components for temperature sensor Sealing set for temperature sensor Comprising: one PEH joint pipe, two PE shrink-on sleeves, PE foam and one abrasive strip. for EIGERFLEX® dimensions ( 25/76 and 32/76mm for EIGERFLEX® dimensions ( 40/91 and 75/126mm The electrical components belonging to the frost protection strips must only be installed by an authorized electrical installer. _____ hours' work by electrical installer |  |  |