| Pos. | Quantity | Designation | Item price EUR | Total price EUR |
| --- | --- | --- | --- | --- |
|  |  | COOLMANT District cooling system (ø 125 – 315 mm) Suitable up to max. -20°C / +40°C* and 16 bar, longitudinally watertight, comprising: medium pipe in PE100, insulation made of CFC-free, CO2-blown polyurethane foam (-Value ≤ 0.024 W/mK), seamlessly extruded polyethylene (HD-PE) outer casing, weldable with elastic properties up to –50°C, outer diameter acc. to DIN 8074 Delivered as 6 or 12 m bars COOLMANT District cooling system lfd. m COOLMANT 125/225 mm 5“ lfd. m COOLMANT 140/225 mm - lfd. m COOLMANT 160/250 mm 6“ lfd. m COOLMANT 180/280 mm 7" lfd. m COOLMANT 200/315 mm 8“ lfd. m COOLMANT 225/315 mm 9“ lfd. m COOLMANT 250/355 mm 10“ lfd. m COOLMANT 280/400 mm 11“ lfd. m COOLMANT 315/450 mm 12“ Further dimensions on request *warm water application with limited lifetime and operating pressure (as per DIN 8074) |  |  |

| Pos. | Quantity | Designation | Item price EUR | Total price EUR |
| --- | --- | --- | --- | --- |
|  |  | COOLMANT house lead-in bend, 90° Leg length 1.1 x 1.6m. longitudinally watertight, medium pipe in PE-HD, insulation made of CFC-free CO2-blown rigid polyurethane foam, protective casing in polyethylene (PE-HD). COOLMANT bend 90° Unit: COOLMANT 125/225 mm 5“ Unit: COOLMANT 140/225 mm - Unit: COOLMANT 160/250 mm 6“ Unit: COOLMANT 180/280 mm 7" Unit: COOLMANT 200/315 mm 8“ Unit: COOLMANT 225/315 mm 9“ Unit: COOLMANT 250/355 mm 10“ Unit: COOLMANT 280/400 mm 11“ Unit: COOLMANT 315/450 mm COOLMANT t-piece, angled 45° Leg length 1,0 x 1,0 m, longitudinally watertight, medium pipe in PE-HD (PE100), insulation made of CFC-free CO2-blown rigid polyurethane foam, protective casing in polyethylene (PE-HD). COOLMANT t-piece Unit: COOLMANT 125/225 mm 5“ Unit: COOLMANT 140/225 mm - Unit: COOLMANT 160/250 mm 6“ Unit: COOLMANT 180/280 mm 7" Unit: COOLMANT 200/315 mm 8“ Unit: COOLMANT 225/315 mm 9“ Unit: COOLMANT 250/355 mm 10“ Unit: COOLMANT 280/400 mm 11“ Unit: COOLMANT 315/450 mm |  |  |

| Pos. | Quantity | Designation | Item price EUR | Total price EUR |
| --- | --- | --- | --- | --- |
|  |  | COOLMANT sealing ring consisting of a specially profiled neoprene ring, suitable for: outer diameter of COOLMANT 225 mm outer diameter of COOLMANT 250 mm outer diameter of COOLMANT 280 mm outer diameter of COOLMANT 315 mm outer diameter of COOLMANT 355 mm outer diameter of COOLMANT 400 mm outer diameter of COOLMANT 450 mm Sealing ring for wall leadthrough, impermeable to water pressure < 0.5 bar, seal insert type A (centering) and type C40 (sealing) for core bore or pipe liner, suitable for: outer diameter of COOLMANT 225 mm outer diameter of COOLMANT 250 mm outer diameter of COOLMANT 280 mm outer diameter of COOLMANT 315 mm outer diameter of COOLMANT 355 mm outer diameter of COOLMANT 400 mm outer diameter of COOLMANT 450 mm |  |  |
| Pos. | Quantity | Designation | Item price EUR | Total price EUR |
|  |  | COOLMANT shrink-on end cap for damp zones Heat-shrink closure for house lead-ins, consisting of: molecular cross-linked and modified polyolefin, coated with sealing adhesive with temperature resistance up to 125°C. Including temperature measuring strip and abrasive strip. or End cap for COOLMANTfor dry zones suitable for: Unit: COOLMANT 125/225 mm 5“ Unit: COOLMANT 140/225 mm - Unit: COOLMANT 160/250 mm 6“ Unit: COOLMANT 180/280 mm 7" Unit: COOLMANT 200/315 mm 8“ Unit: COOLMANT 225/315 mm 9“ Unit: COOLMANT 250/355 mm 10“ Unit: COOLMANT 280/400 mm 11“ Unit: COOLMANT 315/450 mm |  |  |

| Pos. | Quantity | Designation | Item price EUR | Total price EUR |
| --- | --- | --- | --- | --- |
|  |  | COOLMANT sleeves, electrofusion sleeve to connect two COOLMANT pipes PE-pipe 125 x 11.4 mm 140 x 12.7 mm 160 x 14.6 mm 180 x 16.4 mm 200 x 18.2 mm 225 x 20.5 mm 250 x 22.7 mm 280 x 25.4 mm 315 x 28.6 mm COOLMANT coupling 90°, electrofusion coupling to connect two COOLMANT pipes, suitable for: PE-pipe 125 x 11.4 mm 140 x 12.7 mm* 160 x 14.6 mm 180 x 16.4 mm 200 x 18.2 mm 225 x 20.5 mm 250 x 22.7 mm 280 x 25.4 mm* 315 x 28.6 mm* * with additional spigot fittings only COOLMANT equal t-piece, electrofusion t-piece to connect two COOLMANT pipes, suitable for: PE-pipe 125 x 11.4 mm 140 x 12.7 mm* 160 x 14.6 mm 180 x 16.4 mm |  |  |
| Pos. | Quantity | Designation | Item price EUR | Total price EUR |
|  |  | 200 x 18.2 mm 225 x 20.5 mm 250 x 22.7 mm 280 x 25.4 mm* 315 x 28.6 mm* * with additional spigot fittings only on request any reductions are available COOLMANT joint set Type COOLMANT- COOLMANT for 16 bar pipes, with insulating material: foam packing in polyurethane foam or PE foam, comprising: one PEH joint pipe (for reduction joints: reduced on one side), two PE shrink-on sleeves, foam packing in polyurethane foam or PE foam, and one abrasive strip. Joint set, COOLMANT - COOLMANT for COOLMANT with PUR foam packing, to match the outer diameter: Unit: 225 mm to 225 mm Unit: 250 mm to 250 mm Unit: 250 mm to 225 mm Unit: 280 mm to 280 mm Unit: 280 mm to 250 mm Unit: 315 mm to 315 mm Unit: 315 mm to 250 mm Unit: 355 mm to 355 mm Unit: 355 mm to 315 mm Unit: 400 mm to 400 mm Unit: 400 mm to 355 mm Unit: 450 mm to 450 mm Unit: 450 mm to 400 mm |  |  |