| Pos. | Quantity | Designation | Item price EUR | Total price EUR |
| --- | --- | --- | --- | --- |
|  |  | CASAFLEX® district heating pipe, flexible, self-compensating, delivered in rings or on drums, incl. factory test, for operational temperatures up to max. 180ºC, 25 bar, consisting of an inner corrugated pipe in stainless steel with helical corrugation for optimal flow characteristics, monitoring wires for end-to-end monitoring of the entire pipe, insulation made of continuously manufactured, CFC-free, pentane-blown flexible polyisocyanurate rigid foam (PIR), PE film and sinusoidally corrugated, seamlessly extruded-on polyethylene (PE-LD) outer casing. CASAFLEX® UNO cont. m CASAFLEX® 22/91 DN 20 cont. m CASAFLEX® 30/91 DN 25 cont. m CASAFLEX® 30/111 PLUS DN 25 cont. m CASAFLEX® 39/111 DN 32 cont. m CASAFLEX® 39/126 PLUS DN 32 cont. m CASAFLEX® 48/111 DN 40 cont. m CASAFLEX® 48/126 PLUS DN 40 cont. m CASAFLEX® 60/126 DN 50 cont. m CASAFLEX® 60/142 PLUS DN 50 cont. m CASAFLEX® 75/142 DN 65 cont. m CASAFLEX® 75/162 PLUS DN 65 cont. m CASAFLEX® 98/162 DN 80 cont. m CASAFLEX® 127/225 DN 100 CASAFLEX® DUO cont. m CASAFLEX® 22+22/111 DN 20 cont. m CASAFLEX® 30+30/126 DN 25 cont. m CASAFLEX® 39+39/142 DN 32 cont. m CASAFLEX® 48+48/162 DN 40 cont. m CASAFLEX® 60+60/182 DN 50 CASAFLEX® pipe warning tape for underground installation of district heating pipes, printed with the words "Caution! District heating pipe!" ________ m warning tape |  |  |
| Pos. | Quantity | Designation | Item price EUR | Total price EUR |
|  |  | CASAFLEX®-connector for transition to internal pipes in the building/structure, comprising: bearing ring, graphite seal, connection piece, pressure ring and hexagon socket screws. Suitable for: CASAFLEX® UNO Unit for CASAFLEX® 22/91 DN 20 Unit for CASAFLEX® 30/91 and 30/111 PLUS DN 25 Unit for CASAFLEX® 39/111 and 39/126 PLUS DN 32 Unit for CASAFLEX® 48/111 and. 48/126 PLUS DN 40 Unit for CASAFLEX® 60/126 and 60/142 PLUS DN 50 Unit for CASAFLEX® 75/142 and 75/162 PLUS DN 65 Unit for CASAFLEX® 98/162 DN 80 Unit for CASAFLEX® 127/225 DN 100 CASAFLEX® DUO Unit for CASAFLEX® 22+22/111 DN 20 Unit for CASAFLEX® 30+30/126 DN 25 Unit for CASAFLEX® 39+39/142 DN 32 Unit for CASAFLEX® 48+48/162 DN 40 Unit for CASAFLEX® 60+60/182 * DN 50 *the CASAFLEX® DUO dimension is implemented with two connectors, type CASAFLEX® UNO |  |  |
| Pos. | Quantity | Designation | Item price EUR | Total price EUR |
|  |  | CASAFLEX® protective cap for connector To protect the pipe ends in buildings or shafts, comprising two corrosion-resistant plastic half shells, suitable for: CASAFLEX® UNO Unit for CASAFLEX® 22/91 DN 20 Unit for CASAFLEX® 30/91 DN 25 Unit for CASAFLEX® 30/111 PLUS DN 25 Unit for CASAFLEX® 39/111 DN 32 Unit for CASAFLEX® 39/126 PLUS DN 32 Unit for CASAFLEX® 48/111 DN 40 Unit for CASAFLEX® 48/126 PLUS DN 40 Unit for CASAFLEX® 60/126 DN 50 Unit for CASAFLEX® 60/142 PLUS DN 50 Unit for CASAFLEX® 75/142 DN 65 Unit for CASAFLEX® 75/162 PLUS DN 65 Unit for CASAFLEX® 98/162 DN 80 Unit for CASAFLEX® 127/225 DN 100 CASAFLEX® DUO Unit for CASAFLEX® 22+22/111 DN 20 Unit for CASAFLEX® 30+30/126 DN 25 Unit for CASAFLEX® 39+39/142 DN 32 Unit for CASAFLEX® 48+48/162 DN 40 |  |  |
| Pos. | Quantity | Designation | Item price EUR | Total price EUR |
|  |  | CASAFLEX joint set (CFL-CFL) for transition from CASAFLEX to CASAFLEX, comprising: PE-HD shrink joint, shrink-on sleeves, impact plug, foam hole seals, PUR foam cartridge and installation instructions. Unit for outer pipe ( 91 mm Unit for outer pipe ( 111 mm Unit for outer pipe ( 126 mm Unit for outer pipe ( 142 mm Unit for outer pipe ( 162 mm Unit for outer pipe ( 182 mm Unit for outer pipe ( 225 mm CASAFLEX joint set (CFL-plastic casing pipe) for transition from CASAFLEX to plastic casing pipe, comprising: PE-HD shrink joint, shrink-on sleeves, impact plug, foam hole seals, PUR foam cartridge and installation instructions. Unit for outer pipe ( CFL 91 mm - plastic casing pipe 110 mm Unit for outer pipe ( CFL 111 mm - plastic casing pipe 110 mm Unit for outer pipe ( CFL 91 mm - plastic casing pipe 125 mm Unit for outer pipe ( CFL 111 mm - plastic casing pipe 125 mm Unit for outer pipe ( CFL 126 mm - plastic casing pipe 125 mm Unit for outer pipe ( CFL 126 mm - plastic casing pipe 140 mm Unit for outer pipe ( CFL 142 mm - plastic casing pipe 140 mm Unit for outer pipe ( CFL 142 mm - plastic casing pipe 160 mm Unit for outer pipe ( CFL 162 mm - plastic casing pipe 160 mm Unit for outer pipe ( CFL 162 mm - plastic casing pipe 180 mm Unit for outer pipe ( CFL 182 mm - plastic casing pipe 180 mm Unit for outer pipe ( CFL 182 mm - plastic casing pipe 200 mm Unit for outer pipe ( CFL 225 mm - plastic casing pipe 225 mm |  |  |
| Pos. | Quantity | Designation | Item price EUR | Total price EUR |
|  |  | CASAFLEX® Y-pipe Pre-insulated longitudinally watertight connecting component between two single plastic casing pipes and one CASAFLEX® DUO pipe. Steel medium pipe, suitable for: CASAFLEX® DUO Unit for CFL 22+22/111 to plastic casing pipe 26.9 x 90/110 Unit for CFL 30+30/126 to plastic casing pipe 33.7 x 90/110 Unit for CFL 39+39/142 to plastic casing pipe 42.4 x 110/125 Unit for CFL 48+48/162 to plastic casing pipe 48.3 x 110/125 Unit for CFL 60+60/182 to plastic casing pipe 60.3 x 125/140 CASAFLEX® monitoring wire connector set for monitoring wire connections at transitions from CASAFLEX to CASAFLEX or CASAFLEX to plastic casing pipe in joints or assembly T-pieces, comprising: monitoring wires, crimp-type collars, spacers and shrink-on sleeves. One monitoring wire connection set is required for each joint or assembly T-piece Unit to fit all dimensions of joints or assembly T-pieces. CASAFLEX® sealing ring Made of neoprene rubber, with special profile, to seal building and shaft lead-ins. Unit for casing pipe ( 91mm Unit for casing pipe ( 111mm Unit for casing pipe ( 126mm Unit for casing pipe ( 142mm Unit for casing pipe ( 162mm Unit for casing pipe ( 182mm Unit for casing pipe ( 225mm CASAFLEX® connection box for loop wiring at pipe end points, water splash-resistant housing, type of protection IP 54/65, material: Duroplast, with connection terminals. Unit CASAFLEX® measurement connection box, water splash-resistant housing, type of protection IP 54/65, material: Duroplast, with connection terminals and plug socket to connect a manual testing device, type: WIREM BS-MH2. |  |  |